## Slide 1: Ecological Restoration and Rehabilitation: Standards and Case Studies
FROM EUROPE AND CHINA
Mendes A; Fabião A; Jihanua L; Zhang A; Xu F; Baiyinbaoligao; Ferreira T; Rabaça J
Xuzhou International Forum on Green Urban Development
10th to 12th of June 2019
Notes: Cover page

## Slide 2: Summary of contents
Drivers of restoration in China
International definitions of restorations practices
Case Studies
On-line inquiry – results and future work
Definitions of restoration practices in Europe
Drivers of restoration in Europe
Global and Regional policy drivers of restoration

## Slide 3: Global and Regional Policy Drivers of Restoration
Restoration
Convention for Biological Diversity
Convention on the Protection and Use of Transboundary Watercourses and International Lakes
Convention on International Trade of Endangered Species of Wild Flora and Fauna
Convention on Conservation of Migratory Species of Wild Animals
Convention on Wetlands of International Importance Especially as Waterfowl Habitat
UN Biodiversity Plan
Sustainable Development Goals
Restoration – UN next decade priority
Notes: Lead to: Improved water protection in the EU; Development of a dynamic, world-leading water sector; Building block for the EU
to spark green and blue growth and become more resource efficient
In: http://www.ecrr.org/Publications/tabid/2624/mod/11083/articleType/ArticleView/articleId/3052/Default.aspx
A range European Directives or national legislation/ policies and implementation programmes have led to an actual demand for river restoration tools and techniques and these can generally be grouped into two categories:
1. Those which drive the delivery or river and catchment restoration, because restoration offers a means of meeting the objective of the Directive or policy
2. Those which support the delivery of river restoration (here highlighted in blue), through wider environmental improvements, such as water quality, without which a restoration project might fail.
Aditional Information about Water Framework Directive interactions with other legislative pieces in http://www.epa.ie/water/watmg/wfd/#.Vs1h77SYM_U:
The Water Framework Directive is linked to a number of other EU directives in several ways. These include Directives relating to the protection of biodiversity (Birds and Habitats Directives), directives related to specific uses of waters (drinking water, bathing waters and urban waste water directives) and to directives concerned with the regulation of activities undertaken in the environment (Industrial Emissions and Environmental Impact Assessment directives). More recent directives on topics such as Floods and the Marine Strategy Framework have significant linkages with the WFD which is also supplemented by the Priority Substances Directive and the Groundwater Directive. The Nitrates Directive forms an integral part of the Water Framework Directive and is one of the key instruments in the protection of waters against agricultural pressures. The Sustainable Use of Pesticides and the Sewage Sludge Directives also provide for the control of materials applied to land.

## Slide 4: Drivers of Restoration in Europe
In “Review of policy river restoration drivers in Europe” – European Centre for River Restoration -
Restoration
Birds
Directive
Habitats
Directive
Water Framework Directive
Rural Development Programmes
Climate Change Adaptation Policy
Land Use Planning Policies
Floods
Directive
Nitrates Directive
Groundwater Directive
Common Agricultural Policy
Notes: Implementation of the Water Framework Directive, 1st cycle 2009-2015: €300 billion
Construction, renewal and maintenance of urban water infrastructure: €90 billion annually
Research & Development: €9 billion
 Significant underinvestment in water
Lead to: Improved water protection in the EU; Development of a dynamic, world-leading water sector; Building block for the EU
to spark green and blue growth and become more resource efficient
In: http://www.ecrr.org/Publications/tabid/2624/mod/11083/articleType/ArticleView/articleId/3052/Default.aspx
A range European Directives or national legislation/ policies and implementation programmes have led to an actual demand for river restoration tools and techniques and these can generally be grouped into two categories:
1. Those which drive the delivery or river and catchment restoration, because restoration offers a means of meeting the objective of the Directive or policy
2. Those which support the delivery of river restoration (here highlighted in blue), through wider environmental improvements, such as water quality, without which a restoration project might fail.
Aditional Information about Water Framework Directive interactions with other legislative pieces in http://www.epa.ie/water/watmg/wfd/#.Vs1h77SYM_U:
The Water Framework Directive is linked to a number of other EU directives in several ways. These include Directives relating to the protection of biodiversity (Birds and Habitats Directives), directives related to specific uses of waters (drinking water, bathing waters and urban waste water directives) and to directives concerned with the regulation of activities undertaken in the environment (Industrial Emissions and Environmental Impact Assessment directives). More recent directives on topics such as Floods and the Marine Strategy Framework have significant linkages with the WFD which is also supplemented by the Priority Substances Directive and the Groundwater Directive. The Nitrates Directive forms an integral part of the Water Framework Directive and is one of the key instruments in the protection of waters against agricultural pressures. The Sustainable Use of Pesticides and the Sewage Sludge Directives also provide for the control of materials applied to land.

## Slide 5: Drivers of Restoration in China
Restoration
National Comprehensive Plan on Water Resources
2010-2030
River and Lake Chief System
Water Law of PRC
1988 (2016)
Promoting the Development of Ecological Civilization (2015)
Water Pollution Prevention and Control Action Plan
2015
The new Environmental Protection Law (2015)
Three Red Lines of Most Stringent Water Resources Management (2012)

## Slide 6: International definitions of restorations practices
McDonald, T., Gann, G.D., Jonson, J., Dixon, K.W. 2016. International Standards for the Practice of Ecological Restoration - Including Principles and Key Concepts. First Edition. Society for Ecological Restoration, Washington D.C.
Free download at:
http://www.ser.org/?page=SERStandards
“Ecological restoration is the process of assisting the recovery of an ecosystem that has been degraded, damaged or detroyed” (Society for Ecological Restoration, 2004)

## Slide 7
Adapted from McDonald, T., Jonson, J., Dixon, K.W. 2016. National standards for the practice of ecological restoration in Australia. Restoration Ecology 24:S4-S32. DOI: 10.1111/rec.12359
SER standards consider 3 levels of ecological restoration:
Full recovery: key ecosystem attributes similar to those of the reference ecosystem.
Partial recovery: ecosystem attributes have improved but do not closely resemble those of the reference ecosystem.
Ecosystem maintenance: activities applied after full recovery to stop processes of ecological degradation.
Notes: Restore: to recover the natural composition, structure, processes and functions of a river, thereby allowing it to once again achieve full integrity and preserve its self-regulated dynamic balance
Rehabilitate: to recover the composition, structure, processes and functions that are as close as possible to the river’s natural conditions (reference scenario…)
Mitigate: to achieve a status that is significantly different from river’s natural state, but reaches a compromise with the inevitable limitations which the river is subjected.

## Slide 8
Source: McDonald, T., Jonson, J., Dixon, K.W. 2016. National standards for the practice of ecological restoration in Australia. Restoration Ecology 24:S4-S32. DOI: 10.1111/rec.12359
SER Five star classification system helps to track progress towards project goals over time. It uses six key ecosystem attributes to measure progress towards full restoration:
Species composition
Structural diversity (=Community structure)
Ecosystem function
External Exchanges
Absence of threats
Physical conditions

## Slide 9: Definitions of Restoration in Europe
Restore: to recover the natural composition, struture, processes and functions of a river, thereby allowing it to once again achieve full integrity and preserve its self-regulated dynamic balance
Rehabilitate: to recover the compostion, struture, processes and functions that are as close as possible to the river’s natural conditions (reference scenario…)
Mitigate: to achive a status that is significantly different from river’s natural state, but reaches a compromise with the inevitable limitations which the river is subjected.

## Slide 10
CASE STUDY – PAUL DA GOUCHA, PORTUGAL
ENVIRONMENTAL REHABILITATION
ENVIRONMENTAL EDUCATION
TRIGGER / IMPROVE NATURAL RIPARIAN VEGETATION COLONIZATION
REHABILITATE THE FEEDING, NESTING AND RESTING AREA FOR BIRDS
Notes: TARGET: restoration of a willow dominated wetland
GOALS: multi strata, resilient, native wetland woodland; improve bird habitat; environmental education
OBJECTIVES: cessation of litter dumping in 1 year; reduce abundance of invasive plants; trigger / improve natural riparian vegetation colonization; restore the feeding, nesting and resting area for birds

## Slide 11
PLANNING
AND
DESIGN

## Slide 12: Case Study – Alpiarça - Portugal
1993

## Slide 13: Developed activities - Direct Cost: 44 893€
Debris clean-up and soil reprofiling

## Slide 14: Native Plant Propagation
The lack of suitable plant material from the same geographic region for pilot restoration projects was addressed

## Slide 15: Developed activities Total Cost: 44 893€
Exotic species removal (Arundo donax)
Tree and shrub plantation
February 2008

## Slide 16
MONITORING
Global average survival after 9 years was 70% (stolen plants were recorded, but counted as dead).
About 7% of the plants were stolen with Populus nigra (23% of the plants stolen) and Arbutus unedo (17% stolen) being the the most attractive for robbers.
Chart: Survival (%)
| A. glutinosa | A. unedo | C. australis | F. alnus | F. angustifolia | P. pinea | P. nigra | Q. suber | S. alba | S. atrocinerea | S. salviifolia | T. africana
Average survival by species (2008) | 56.8627 | 52.7778 | 95.3488 | 60.8696 | 70.4225 | 75.6757 | 53.75 | 81.8182 | 63.8889 | 59.375 | 76.4706 | 100
Average survival by species (2014) | 35.2941 | 22.2222 | 62.7907 | 4.3478 | 74.6479 | 67.5676 | 48.75 | 59.0909 | 101.3889 | 100 | 52.9412 | 4
Average survival by species (2017) | 41.1765 | 27.7778 | 76.7442 | 0 | 81.6901 | 148.6486 | 42.5 | 118.1818 | 77.7778 | 109.375 | 74.5098 | 0
Global average survival (2014) | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957 | 60.6957
Global average survival (2017) | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391 | 69.7391
CEWP Workshop on River Restoration, 6-7 February 2018, Beijing

## Slide 17
MONITORING
Most of the highest values observed 9 years after planting account for natural regeneration from the seed bank and adjacent reproductive tree sources.
Populus nigra presented the highest average DBH (27.2±2.0 cm), followed by Alnus glutinosa (16.1±1.7 cm) and Salix alba (15.5±1.3 cm).
CEWP Workshop on River Restoration, 6-7 February 2018, Beijing
Chart: DBH (cm)
| F. angustifolia | S. salviifolia | S. atrocinerea | S. alba | P. nigra | A. glutinosa | P. pinea | C. australis
Average DBH after 9 years | 7.7167 | 7.1793 | 9.5469 | 15.4827 | 27.2029 | 16.07 | 10.7937 | 1.6575
Chart: 
| 0-2,5 | 2,5-5 | 5-7,5 | 7,5-10 | 10-12,5 | 12,5-15 | 15-17,5 | 17,5-20 | 20-22,5 | 22,5-25 | 25-27,5 | 27,5-30 | 30-32,5 | 32,5-35 | 35-37,5 | 37,5-40
Frequency | 43 | 35 | 36 | 42 | 29 | 25 | 25 | 14 | 16 | 7 | 5 | 7 | 1 | 3 | 5 | 2
% cumulative frequency | 0.14576 | 0.26441 | 0.38644 | 0.52881 | 0.62712 | 0.71186 | 0.79661 | 0.84407 | 0.89831 | 0.92203 | 0.93898 | 0.96271 | 0.9661 | 0.97627 | 0.99322 | 1
Frequency histogram with DBH class distribution 9 years after plantation
Notes: Global DBH class distribution after 9 years shows a gradual frequency reduction from the lower class to the higher class, i. e., a DBH distribution close to that typical of a unevenaged, multicohort stand with natural regeneration

## Slide 18: Bioengineering Techniques

## Slide 19: Live fascines

## Slide 20
Live fascines

## Slide 21: Wattle fences

## Slide 22
Wattle fences

## Slide 23: Brush mattresses

## Slide 24: Brush mattresses

## Slide 25: Planted coconut fiber rolls

## Slide 26: Planted coconut fiber rolls

## Slide 27
MONITORING - SOIL BIOENGINEERING
Poles and live cuttings of Salix atrocinerea collected on the undisturbed sections of the Paul da Goucha
Variable success, related mainly to the proximity to water and the use of live cuttings instead of rooted plants in the driest locations.
A, B e C: Cribwall
D: Brush mattress
E: planted coconut fiber rolls
F: Wattle fences
G: Live fascines
A
B
C
G
F
E
D
CEWP Workshop on River Restoration, 6-7 February 2018, Beijing

## Slide 28
http://seraustralasia.com/wheel/wheel.html
2008, after 6 months
2017, after 9 years
★★★☆☆
Adjacent threats being managed or mitigated and very low threat from undesirable species onsite. A moderate subset of characteristic native species are established and some evidence of ecosystem functionality commencing. Improved connectivity in evidence.
EVALUATION

## Slide 29
SEPTEMBER 2011
AUGUST 2014
FEBRUARY 2008

## Slide 30: 中欧水平台环境修复项目问卷调研 CEWP Restoration projects inquiry
In the context of China Europe Water Platform, the University of Évora, the China Institute of Water Resources and Hydro-power Research and Tongji University are promoting an on-line inquiry to make an evaluation of restoration projects developed in Europe and China, with the objective of contributing to increase restoration standards. By answering to this questionnaire, you will be contributing to a policy study that wishes to give support to European and Chinese policy makers on the most appropriate restoration standards to use when developing this type of project. The inquiry is targeted to restoration projects implemented in freshwater ecosystems.
https://pt.surveymonkey.com/r/8XYGB36

## Slide 31: Impact of policy on restoration projects
China
Europe

## Slide 32
3 Star
Absence of Threats
Physical Conditions
Species composition
4 Star
Strutural composition
2 Star
Ecosystem function
External Exchanges
Notes: Example how to present some statistics or numerical facts.

## Slide 33
3 Star
Absence of Threats
Physical Conditions
2 Star
Species composition
Strutural Diversity
1 Star
Ecosystem function
External Exchanges
Notes: Example how to present some statistics or numerical facts.

## Slide 34
Thank you!
www.cewp.eu
Twitter @ChinaEUwater
Notes: Thank you page – web + place for additional contact info. Change background colour by right-clicking → Edit background Fill → colour

## Slide 35
谢谢!
Twitter @ChinaEUwater
www.cewp.eu
Notes: Thank you page – web + place for additional contact info. Change background colour by right-clicking → Edit background Fill → colour

## Slide 36
aimendes@uevora.pt
University of Évora
Portugal
PhD, Professor
https://pt.surveymonkey.com/r/8XYGB36
Notes: Change background image by right-clicking → Edit background Picture fill → From file